## Slide 1: Fixed-Point Optimization of Atoms & Density in DFT
L. D. Marks
Department of Mat. Sci. & Eng.
Northwestern University

## Slide 2: Fundamentals
A substantial fraction of the world computing is doing DFT calculations.
IBM Blue Gene
Increasingly large calculations are being done by experimentalists. Need robust, reliable, accurate and fast algorithms.
Enterkin et. al., Nature Materials, 2010

## Slide 3: Converging many DFT codes
The DFT literature (published, unpublished, listserver) is full of “fudges” and confusion about getting calculations to converge.
  “Mixing factors”
  Run calculations at 2000K (metals)

## Slide 4: Self-consistent field (SCF) cycle
SCF cycle
Start with r(r)
Calculate Veff (r) =f[r(r)]
Mix F(r(r)) & r(r)

## Slide 5: DFT
Density
Potential
Solve eigenvectors
values
New Density
Mix Density
Converged?
No
Atomic Positions
Inner loop to obtain fixed-point for given atom positions
Outer loop to optimize atomic positions
Yes
No
Minimize Energy
Forces Small

## Slide 6: Current algorithms (pure DFT)
Calculate SCF mapping, time T0
Broyden expansion for fixed-point problem, self-consistent density, NSCF iterations
BFGS is most common for optimizing the atomic positions (Energy), NBFGS
Time scales as NSCF*NBFGS*T0

## Slide 7: Double-Loop
Born-Oppenheimer Surface
Energy Contours
Fixed-Point for Density
BFGS step

## Slide 8: Convergence
Classic QN convergence results*:
  NSCF scales as number of clusters of eigenvalues of the dielectric response, << number of variables
  NBFGS scales as the number of clusters of the force matrix (similar to phonons)
*For instance:
C.T. Kelly, Iterative Methods for Linear and Nonlinear Equations, SIAM, Philadelphia, 1995.
J. Nocedal, S. Wright, Numerical Optimization, New York, 2006.

## Slide 9: Why separate?
Fused problem, number of clusters will be less than the product NSCF*NBFGS
First proposed by Bendt & Zunger (1983), but they could not implement it.

## Slide 10: Fused Loop
Treat the density and atomic positions (as well as hybrid potentials etc as needed) all at the same time.
No restrictions to “special” cases, general algorithm has to work for insulators, metals, semiconductors, surfaces, defects, hybrids….
Few to no user adjustable parameters

## Slide 11: Fused Loop
Born-Oppenheimer Surface
Zero-Force Surface
Energy Contours
Residual Contours

## Slide 12: Broyden Fixed-Point Methods
Solve (r(r,x)-F(r(r,x)),G)=0
Broyden’s “Good Method”
Broyden’s “Bad Method”
Generalizable to multisecant (better, S,Y matrices)
C.G. Broyden, A Class of Methods for Solving Nonlinear Simultaneous Equations, Mathematics of Computation, 19 (1965) 577-593.

## Slide 13: Multisecant Approach
Consider a number of values:
S = (s0,s1,….sn) ; Y=(y0,y1,….yn)
Expand to a simultaneous solution:
BS = Y ; or HY=S
Minimum-Norm Solution
Take Hk=I

## Slide 14: Reality Checkpoint
In a linear model both “Good” and “Bad” methods have been shown to be superlinearly convergent, and by induction so will a linear combination*.
Hence they should behave comparably.
They don’t, Good is unstable in DFT
Hence the linear model is misleading
*For instance:
C.T. Kelly, Iterative Methods for Linear and Nonlinear Equations, SIAM, Philadelphia, 1995.
J. Nocedal, S. Wright, Numerical Optimization, New York, 2006.

## Slide 15: Phase Transitions: Jacobian can change discontinuously
Electronic configuration of F() in the second step as a function of the size of the first Pratt step for an Fe atom, with the 4s occupancy within the muffin-tins in black (x10) and the 3d in red
Other examples

## Slide 16: Algorithm Greed
“A greedy algorithm always makes the choice that looks best at the moment. That is, it makes a locally optimal choice in the hope that this choice will lead to a globally optimal solution.”1
Good Broyden is the optimal greedy algorithm. Hence if the linear model is valid it is best.
Bad Broyden is the least greedy algorithm, optimal if the linear model is not valid.
1T.H. Cormen, C.E. Leiserson, R.L. Rivest, C. Stein, Introduction to Algorithms, MIT Press, Boston, US, 2009.

## Slide 17: What is a greedy algorithm?
A greedy algorithm takes decisions on the basis of information at hand without worrying about the consequences. In many cases “greed is good”, but not always.
Example: make 41c with 25c, 10c, 4c coins
Optimum solution: 25+4x4
Greedy solution: start with 41c, use largest reduction
  25c Remainder 16
  10c Remainder 6
  4c Remainder 2

## Slide 18: Ansatz for Fixed-Point Family
Neither Good nor Bad Broyden work for fused problem
Define the “Fixed-point Broyden Family”
At the solution, Hk is positive definite (stability condition). Therefore chose  to be as small as possible and still yield a positive definite Jacobian. (Optimal greed?)

## Slide 19: Additional Issues
Parameters have an unknown relative scaling
  Scale residue of each part to same L2 norm
is not a descent direction, G is not a true derivative (common fixed point).
  Only apply Trust Region constraints to prior history, and then rarely
No accurate L2 metric
  Use improvement as a guide for unpredicted step size (greed)
  Use matrix form of Shano-Phua scaling to bound
  Prevent over-greedy total steps

## Slide 20: Comparison
Double-Loop calculations
  “Standard” BFGS (PORT library)1
  Spring model initialization2
  MSR1 algorithm, but without atom movement for inner loop
Initialization: normally atomic densities.
No adjusted parameters – i.e. the same results as a novice will obtain.
Room temperature
1Dennis, J. E.; Mei, H. H. W., Journal of Optimization Theory and Applications 1979, 28 (4), 453-482.
2Rondinelli, J.; Bin, D.; Marks, L. D., Computational Materials Science 2007, 40, 345-353.

## Slide 21: Convergence of QN methods
Depends upon clustering of eigenvectors
Rondinelli, J.; Bin, D.; Marks, L. D., Enhancing structure relaxations for first-principles codes: an approximate Hessian approach. Computational Materials Science 2007, 40, 345-353.

## Slide 22: Bulk NiO, on-site hybrid

## Slide 23: Larger Problems, 52 atoms, MgO (111)+H2O (left) & 108 AlFe (right)
J. Ciston, A. Subramanian, L.D. Marks, PhRvB, 79 (2009) 085421.
Lyudmila V. Dobysheva (2011)

## Slide 24: Numbers (unreadable)
Figure | Name | Atoms | Ineq Atoms Na | Atomic Variables Nav | Matrix Size | Density Size Ne | States | Max Change (au) | SCF MSR1 | SCF/Iter BFGS
3 | Ni(OH)2 | 5 | 3 | 2 | 601 | 5644 | 15 | 0.20 | 27 | 108/8
4 | MgO (111)+H2O | 52 | 21 | 42 | 6344 | 28842 | 176 | 2.12 | 241 | 414/23
6 | Al106Fe2 | 108 | 42 | 92 | 5945 | 82643 | 491 | 0.48 | 76 | 148/8
7 | TiO2 (001) 2x2 | 40 | 16 | 35 | 6518 | 25361 | 163 | 0.53 | 156 | 349/13
8 | SrTiO3 (001) 2x1 | 108 | 44 | 96 | 16106 | 65752 | 400 | 2.87 | 480 | 645/40
9 | MgO (111) octapole | 44 | 12 | 20 | 10029 | 17046 | 176 | 1.09 | 92 | 170/13
 |  | 68 | 18 | 32 | 10185 | 21732 | 272 | 1.19 | 109 | 158/10
 |  | 92 | 24 | 44 | 10341 | 26418 | 358 | 1.27 | 138 | 152/10
 |  | 116 | 30 | 56 | 10497 | 31104 | 464 | 1.35 | 151 | 189/14
10 | C2N2H8 | 24 | 6 | 18 | 5764 | 16085 | 26 | 3.20 | 575 | 575/45

## Slide 25: Open questions
Is the ansatz “right”, or is there a better one?
Can the Hessian (Force Matrix) be extracted (to date failed)?
Can the guesstimated dielectric response be better exploited?
Can the fixed-point Broyden family method be used for other problems?
How well will the algorithm work with pseudopotential codes (probably better)?
GNU version (man/woman power /$$ needed)
How to safeguard numerical accuracy degredation?

## Slide 26: Summary
Production level code (not demonstration)
Fused algorithm is ~ twice as fast (sometimes more, in rare cases the same speed)
Works for metals, insulators, atoms, hybrid potentials…
Should work for pseudopotential & other methods
Idiot proof (within reason)
No user input parameters needed in most cases
Many possibilities to improve…..

## Slide 27: Acknowledgements
Peter Blaha Russel Luke TU Wien U. Göttingen

## Slide 28: Questions ?
Diffraction
DFT
Structure
10 nm
NanoCatalysts
It is through science that we prove, but through intuition that we discover. Jules H. Poincaré